¨Home assisted living for the elderly¨ - development of a program –

What do we understand by Home-assisted living?

It is an accessible habitat which provides the elderly with the continuity of an independent life through support services and become more self-sufficient.

Objectives:

PROMOTE among the users:

- AUTONOMY

- SOCIALIZATION AND RELATIONSHIP WITH THE COMMUNITY

- SENSE OF BELONGING

- DIGNITY

- ACTIVE LIFE

- INDEPENDENCE

- PRIVACY

- SECURITY

AVOID:

- ISOLATION AND SOLITUDE

- OVERCROWDING

- SEGREGATION

- ABANDONMENT OF PERSONAL BELONGINGS

- ABANDONMENT OF SOCIAL STANDING

- LOSS OF SELF-CONFIDENCE.

## SPATIAL ORGANIZATION

- Recommendations:

- Flexibility for multiple activities

- Communitarian spaces for social interaction

- Internal ramp: social interaction

- Avoid long distances

- Introduce the use of colours

- Natural lightning

- Wide social sectors for promoting socialization

- Spaces “for observation”

- Spaces divided according to gender.

- Spaces for the relatives.

- Sectorization of the parking lot.

- Semi-closed spaces for climate protection.

- Among others…

DESIGN RECOMMENDATIONS

- Allow the recognition of the private space (affective memories).

- Characterize the users by age or level of independence and autonomy for a better development of interior equipment of the different types of units.

- Double doors in 100% of the units.

- Environment with ergonomic and anthropometric design.

- Introduce concepts such as “clear” and “circulation”

- Window sills: low, no more than 60 cm.

- Accessible storage units.

- Windows at the end of each corridor help orientation.

- Precaution and avoiding accidents: objects out of place, borders, edges, irregularities, reflective walls and floors, dazzling and strong changes of lightning.

- Orientation guide: use of a contrasting colour strip.

- Stairs: 14/16 x 28 cm.

- Internal vegetation

- Gardens with light signs on the floor.

- Path borders with colourful floor tiles (orientation).

- Large windows.

- Balconies, gardens and flowerbeds for gardening.

- Texture and colours on roofs as guide.

- Development of social areas on open spaces, sunny spaces, wind protected.

- Take care of the manoeuvring spaces on the entrance areas.

- Place a seat beside the main entrance for resting if you come with packages o for promoting the socialization.

- All doors would be opened by the same key ( exterior opening A.D.A)

Foresee the presence of pets and their necessary services.

#### PRIVATE SPACE

- Spacious bedrooms for facilitating the making of beds, the cleaning, the lighting, and ventilation. The circulation between the bed and the bathroom must be clear of any obstacle.

- A light for the night

- Position of the bed: able to look at of the window and also able to have a conversation with a visitant.

Bathrooms:

- They can be inside the bedrooms

- Mechanic ventilation must be connected to the same light switch key.

- Wash basin: 80 cm high

- First-aid cupboard and mirror: h =0.60 m a 1.20 m.

- Monocommand taps (domotic habitat)

- Anti-skid floors.

- In case of wheelchair: replace bath for shower with folding chair.

- Shower taps.

- Eliminate the bidet or increase the bathroom area for allowing a 150 cm free turn of the wheelchair.

- Sliding doors with supplementary handles or a push-door open.

- Safety handrails.

- The door would be easily opened from the opposite side.

##### Kitchens

- Integrated flexible kitchens or not, according to the needs of the user.

- Adaptable bathrooms for people in wheelchair or with another assistive technology for locomotion.

Doors: 80cm wide.

- A Space similar to a wardrobe for garbage or dirty clothes, very accessible.

### CIRCULATION

- Avoid steps, loose carpets, and heavy doors or with hydraulic shut and pomela door handles.

- Doors with iron fitting and open from both sides (emergency: internal and external)

- Handrails

- “Path” or primary –secondary circulation path.

### FACILITIES

- Security:

- Ringing and luminous fire, robbery and gas escape alarm

- Sensors

- Emergency bell

- Recommended heating: (controlled by the user): central heating, radiators, T.B heaters, electric radiant floor.

- on/off button for cool/hot air conditioning and open /close mechanisms for light control (light curtains)

- Access control magnetic cards.

- Renewal and purification of air.

- Temperature regularization.

- Complementary alarms: vibratory under the pillow.

- Fire evacuation

### LIGHTING

- Light Control

- Light switches outside rooms to avoid darkness

- Electric switches and sockets: 40-80-100 cm high

- Uniform lighting for avoiding sudden contrasts and dazzling situations.

- General cut-off switch and general thermo magnetic circuit breaker

- Electric Generator